## Slide 1: open twin
Frankfurt University of Applied Sciences, Faculty 2, ©2020 Prof. Dr.-Ing. Peter Thoma
1
Multi physics and multi scale simulation

## Slide 2
Open twin introduction Agenda
Challenges
  1.1 Multi Domain and Multi Scale
  1.2 Computational Resources
  1.3 Data Management / Data Analytics
Open Twin
  2.1 System Requirements Overview
  2.2 Why Open Twin?
  2.3 Architecture and Design
Open Twin Status and Research
Next Steps

## Slide 3
Open twin introduction Agenda
Challenges
  1.1 Multi Domain and Multi Scale
  1.2 Computational Resources
  1.3 Data Management / Data Analytics
Open Twin
  2.1 System Requirements Overview
  2.2 Why Open Twin?
  2.3 Architecture and Design
Open Twin Status and Research
Next Steps

## Slide 4
https://chargedevs.com/features/a-closer-look-at-the-losses-in-ev-motors/
Example: Tesla Model 3: 225 kW, Length = 23 cm, Diameter = 23 cm
1. Engineering Challenges

## Slide 5
https://chargedevs.com/features/a-closer-look-at-the-losses-in-ev-motors/
Electromagnetic performance
1. Engineering Challenges
Thermal management
Lubrication
Noise vibration harshness
Materials (magnets)
Multi body motion
System integration (inverter)
Durability
Example: Tesla Model 3: 225 kW, Length = 23 cm, Diameter = 23 cm

## Slide 6
1. Software Tool Challenges
Physics
Data
HPC
https://chargedevs.com/features/a-closer-look-at-the-losses-in-ev-motors/

## Slide 7
1. Software Tool Challenges
Data
HPC
Physics
https://chargedevs.com/features/a-closer-look-at-the-losses-in-ev-motors/

## Slide 8
1.1 multi domain multi scale simulation
Structural Mechanics
Fluid Dynamics
Thermo- dynamics
Electro-magnetics
Material Science
Strong and weak coupling of multiple
physics domains
Multi Domain

## Slide 9
Geometrical scale / complexity
Material
Part
Product
© ZF
© Mercedes Benz
© Egorov Artem
1.1 multi domain multi scale simulation
Structural Mechanics
Fluid Dynamics
Thermo- dynamics
Electro-magnetics
Material Science
Example: EMC / EMI
Multi Domain
Multi Scale

## Slide 10
System
(MBSE)
Structural Mechanics
Fluid Dynamics
Thermo- dynamics
Electro-magnetics
Material Science
© Toyota
1.1 multi domain multi scale simulation
Multi Fidelity

## Slide 11
Problem specific accuracy requirements
  Realtime  High-precision simulation
Derive system models from physical simulation
  Parameter fittings (physics-based models)
  Surrogate models („Black Box“)
  Model order reduction (often solver specific)
  „Curse of the dimension“  Neural network (AI)
  Adjoint sensitivities  Efficiency
System modelling
  Signal flow modelling, causal (e.g. Simulink)
  Equation based, non causal (e.g. Modelica)
  FMI (causal, co-simulation or model exchange
© Carmaker
1.1 multi domain multi scale simulation
System level Simulation
© Toyota

## Slide 12
Domain 1
Domain 2
1
Sequential
coupling Framework
1.1 multi domain multi scale simulation

## Slide 13
Domain 1
Domain 2
Domain 1
Domain 2
1
Sequential
M1
M2
K
K‘
M=
2
Co-
Simulation
Iterative
coupling Framework
1.1 multi domain multi scale simulation

## Slide 14
Domain 1
Domain 2
Domain 1
Domain 2
Domain 1
Domain 2
Surrogate model 1
Surrogate model 2
1
Sequential
M1
M2
K
K‘
M=
2
Co-
Simulation
3
System
Simulation
Iterative
causal,
non causal
coupling Framework
1.1 multi domain multi scale simulation

## Slide 15
DOF coupling (0D, 1D, 2D, 3D)
Problem specific conservation of properties (average values, maximum values, etc.)
See also: MPCCI, preCICE
Cooperation with suppliers, IP protection
Domain 1
Domain 2
Domain 1
Domain 2
Domain 1
Domain 2
Surrogate model 1
Surrogate model 2
1
Sequential
M1
M2
K
K‘
M=
2
Co-
Simulation
3
System
Simulation
Iterative
causal,
non causal
coupling Framework
1.1 multi domain multi scale simulation

## Slide 16
Convergence and Consistency?
D. Estep , V. Carey , V. Ginting , S. Tavener , T. Wildey:
A posteriori error analysis of multiscale operator decom-position methods for multiphysics models, SIAM Journal on Numerical Analysis 2008 ⇨ Idea: Operator formulation, adjoint problem
DOF coupling (0D, 1D, 2D, 3D)
Problem specific conservation of properties (average values, maximum values, etc.)
See also: MPCCI, preCICE
Cooperation with suppliers, IP protection
Domain 1
Domain 2
Domain 1
Domain 2
Domain 1
Domain 2
Surrogate model 1
Surrogate model 2
1
Sequential
M1
M2
K
K‘
M=
2
Co-
Simulation
3
System
Simulation
Iterative
causal,
non causal
coupling Framework
1.1 multi domain multi scale simulation

## Slide 17
Automation of individual simulations (model preparation, meshing)
Optimization Platform
  Sequential optimization of individual domains ⇨ Multi-domain optimization
  Inefficient due to large differences in runtimes of individual domain simulations
  Improved efficiency due to sequential application of varying levels of fidelity for domain simulations (optimal method is problem dependent ⇨ flexible optimization platform needed)
Optimization Strategies
  Parameter optimization (discrete / continuous, local / global, surrogate models, sensitivities)
  „Space Mapping“, etc.
  Topology optimization
Domain 1
Domain 3
Domain 2
Domain 4
Domain 1
Domain 3
Domain 2
Domain 4
automation and optimization
1.1 multi domain multi scale simulation

## Slide 18
1.1 multi domain multi scale simulation
Source: EnginSoft
Gearbox Lubrication
Open problem:
  Air entrainment at high rotation speed (> 20.000 rpm)
  Some research codes are available, no commercial solution yet
active research example

## Slide 19
1.1 multi domain multi scale simulation
Flexible coupling of simulation domains and simulation codes
Include highly specialized niche solutions
Include research codes
Include in-house codes
Support flexible automation and problem specific optimization
System
(MBSE)
Structural Mechanics
Fluid Dynamics
Thermo- dynamics
Electro-magnetics
Material Science
software requirements for multi physics / multi scale simulation

## Slide 20
1. Software Tool Challenges
Physics
Data
HPC
https://chargedevs.com/features/a-closer-look-at-the-losses-in-ev-motors/

## Slide 21
CUDA,
OpenCL
OpenMP
SIMD
Intel Xeon 8176: 620 Gbit/s, 28 Cores
Nvidia Tesla V100:
- 7200 Gbit/s
- 5120 Cores
Infiniband: 20 Gbit/s
MPI
Parallel
(distributed)
file system
Distribution of data / load balancing
Data transfer performance
⇨ Development of specific algorithms
1.2 computational resources
high performance computing architecture

## Slide 22
CUDA,
OpenCL
OpenMP
SIMD
Intel Xeon 8176: 620 Gbit/s, 28 Cores
Nvidia Tesla V100:
- 7200 Gbit/s
- 5120 Cores
Infiniband: 20 Gbit/s
MPI
Parallel
(distributed)
file system
Distribution of data / load balancing
Data transfer performance
⇨ Development of specific algorithms
1.2 computational resources
high performance computing architecture
Local computation resources (e.g. laptops) are often not sufficient  compute cluster / cloud

## Slide 23
Images © Dassault Systèmes
Example (explicit transient simulation – Finite Difference scheme)
visualization
1.2 computational resources

## Slide 24
Example (explicit transient simulation – Finite Difference scheme)
  25e9 mesh cells ⇨ 150e9 degrees of freedom ⇨ 1.200 GB of data per time step,
  30.000 time steps ⇨ 36.000 TB simulation data
 Integration of simulation and visualization
 Visualization and computation of secondary quantities is a HPC problem
Images © Dassault Systèmes
visualization
1.2 computational resources

## Slide 25
Images © Dassault Systèmes
Data
Rendering
Filtering,
Mapping
Data
Source
Pixel Stream
Domain
specific
data
Interaction
Data
Data
Data
Data
Micro Services
Visualization
Visualization
Visualization
Visualization
visualization
1.2 computational resources
Open and modular architecture
Only the data source is domain specific
Visualization of large data sets on any device

## Slide 26
Images © Dassault Systèmes
Rendering
Filtering,
Mapping
Data
Source
Pixel Stream
Domain
specific
data
Interaction
Micro Services
Open and modular architecture
Only the data source is domain specific
Visualization of large data sets on any device
Real-time visualization during the simulation
Data
Visualization
Visualization
Visualization
Visualization
Data
Data
Data
Data
Solver
Solver
Solver
Solver
visualization
1.2 computational resources

## Slide 27
1. Software Tool Challenges
https://chargedevs.com/features/a-closer-look-at-the-losses-in-ev-motors/
Physics
HPC
Data

## Slide 28
Data of arbitrary type and source „Variety“
Large amounts of data „Volume“
  Very large data sets (e.g. simulation results)
  Many smaller data sets (e.g. real time sensor data)
High performance access to data „Velocity“
  Visualization, processing of sensor data, etc.
Immutable data (certification) „Validity“
Maximum gain of information from data „Value“
Distributed data storage
Data security
Simulation data management (revisions)
Big-Data
simulation data management
1.3 data management data analytics

## Slide 29
1.3 data management data analytics
Data stored in file system does not allow for efficient data analysis  Data Base
Additional meta data can be generated at any time by running distributed analysis on database (lambda layer)  Flexible Analytics
Potential applications: Knowledge capture, statistics, training data for AI, …, ?
vs.

## Slide 30
Open twin introduction Agenda
Challenges
  1.1 Multi Domain and Multi Scale
  1.2 Computational Resources
  1.3 Data Management / Data Analytics
Open Twin
  2.1 System Requirements Overview
  2.2 Why Open Twin?
  2.3 Architecture and Design
Open Twin Status and Research
Next Steps





## Slide 31
2.1 System requirements overview
Physics
Data
HPC
https://chargedevs.com/features/a-closer-look-at-the-losses-in-ev-motors/

## Slide 32
System Simulation (Model Based Systems Engineering)
Integration Platform (Automation / Optimization)
Multi-Domain / Multi-Scale Simulation
Visualization
Model
Preparation
High Performance Computing (HPC)
Storage and Processing of Large Data Sets (Big Data)
2.1 System requirements overview

## Slide 33
Open twin introduction Agenda
Challenges
  1.1 Multi Domain and Multi Scale
  1.2 Computational Resources
  1.3 Data Management / Data Analytics
Open Twin
  2.1 System Requirements Overview
  2.2 Why Open Twin?
  2.3 Architecture and Design
Open Twin Status and Research
Next Steps






## Slide 34
2.2 why open twin
There are lots of powerful solutions available already – why Open Twin?
Are we going to re-invent the wheel?

## Slide 35
2.2 why open twin
No! The Open Twin integrates existing technology
to provide more powerful solutions

## Slide 36
2.2 why open twin
A large variety of commercial, in-house or academic solutions are available (e.g. Onelab, getDP, Moose, ngsolv,…)
In-house or academic tools often don’t have the necessary infrastructure (pre- / post-processing, data management) to support industrial application
When developing research codes, often simple infrastructures are developed repeatedly (re-inventing the wheel)
Commercial solutions are often not open enough to integrate third party solutions
Open Twin provides existing solutions with an infrastructure to handle:
  complex (coupled) physics problems
  large amounts of data
  heavy computations
  many computations
The purpose of open Twin is integration

## Slide 37
2.2 why open twin
Distributed application
Supports local workstations, compute cluster, cloud
Data is stored in a data base rather than in the file system
Minimize data transfer (map & reduce approach, remote visualization)
Open – allow for integration of existing technology
Open source – freely available for commercial and non-commercial use
Key capabilities of open Twin - Unique combination

## Slide 38
Open twin introduction Agenda
Challenges
  1.1 Multi Domain and Multi Scale
  1.2 Computational Resources
  1.3 Data Management / Data Analytics
Open Twin
  2.1 System Requirements Overview
  2.2 Why Open Twin?
  2.3 Architecture and Design
Open Twin Status and Research
Next Steps







## Slide 39: 2.3 architecture and design
User Interface
(1)
Versioned API
Model management
(1)
Generic visualization
(1...n)
Meshing
(1…n)
Result visualization
(1…n)
Simulator plugin
(1…n)
Automation and Optimization
(1)
Data storage
Versioned API
Versioned API
Versioned API
Versioned API
Versioned API
Versioned API
Microservice Framework
Microservice:
Serves a business purpose (contract ⇨ testing)
API hides implementation and technology
May contain a UI
Small
Easy to replace
Developed by one team

## Slide 40
2.3 architecture and design
Advantages:
  Provide scalability for complex systems
  Support for mixed programming languages & environments
  Development teams focus on individual microservices
  Develop, test, and deploy versioned microservices independently
  Support for multiple versions of services
  Support for mix of different license models (incl. GPL)
Disadvantages:
  Distributed system adds extra complexity and overhead
Microservices = Concept for software modularization

## Slide 41
2.3 architecture and design
Microservices software complexity
Productivity
Software Complexity
Monolithic
Architecture
Microservice
Architecture
For small systems,
Microservices architecture
introduces overhead
As complexity increases,
reduced coupling better
maintains productivity

## Slide 42
2.3 architecture and design
microservices pipeline
Developer 1
Developer 2
Developer 3
Develop
Staging SCM
Service Integration
Test
Master SCM
Service A v1
Service A v2
…
Service A vN
Service A
Develop
Develop
Service B
Service B v1
Service B v2
…
Service B vN
vN
System
Integration Test
Deploy
.
.
.
Unit Test
Unit Test
Unit Test

## Slide 43: 2.3 architecture and design
User Interface
(1)
Versioned API
Model management
(1)
Generic visualization
(1...n)
Meshing
(1…n)
Result visualization
(1…n)
Simulator plugin
(1…n)
Automation and Optimization
(1)
Data storage
Versioned API
Versioned API
Versioned API
Versioned API
Versioned API
Versioned API
Microservice Framework

## Slide 44: 2.3 architecture and design
User Interface
(1)
Versioned API
Model management
(1)
Generic visualization
(1...n)
Meshing
(1…n)
Result visualization
(1…n)
Simulator plugin
(1…n)
Automation and Optimization
(1)
Data storage
Versioned API
Versioned API
Versioned API
Versioned API
Versioned API
Versioned API
Microservice Framework

## Slide 45
2.3 architecture and design
Microservice infrastructure based on Rust framework
Integration of microservices with C++ libraries / DLLs
Communication between microservices through http / REST
Communication data will be transmitted as Json strings
Dedicated layer for conversion of C++ data types from and to Json
Microservice framework allows to encapsulate generic DLLs into microservices
Synchronous and asynchronous communication
Can be deployed either on one node or distributed (http communication)
Microservice Framework

## Slide 46: 2.3 architecture and design
User Interface
(1)
Versioned API
Model management
(1)
Generic visualization
(1...n)
Meshing
(1…n)
Result visualization
(1…n)
Simulator plugin
(1…n)
Automation and Optimization
(1)
Data storage
Versioned API
Versioned API
Versioned API
Versioned API
Versioned API
Versioned API
Microservice Framework

## Slide 47
2.3 architecture and design
Data storage based on No-SQL database MongoDB Community Server (high performance / big data)
Document oriented database with powerful search capabilities
Potentially distributed database server architecture
Provision of API library to be linked to application modules
Data stored in immutable versioned objects
Data objects consist of meta data (Bson) and optionally large binary data
Large data to be stored in file system directly. File index stored in database
Local database services running on local file systems to transfer files if needed
File storage transparent to application, handled through API
Support of map/reduce pattern for efficient management of large data sets
Data Storage

## Slide 48: 2.3 architecture and design
User Interface
(1)
Versioned API
Model management
(1)
Generic visualization
(1...n)
Meshing
(1…n)
Result visualization
(1…n)
Simulator plugin
(1…n)
Automation and Optimization
(1)
Data storage
Versioned API
Versioned API
Versioned API
Versioned API
Versioned API
Versioned API
Microservice Framework

## Slide 49
2.3 architecture and design
Generic user interface module
Separated from other modules via API
Can be replaced by other realizations of API
Current implementation done in C++ based on Qt
Ribbon style toolbar concept
Flexible support of color schemes and styles
user Interface

## Slide 50: 2.3 architecture and design
User Interface
(1)
Versioned API
Model management
(1)
Generic visualization
(1...n)
Meshing
(1…n)
Result visualization
(1…n)
Simulator plugin
(1…n)
Automation and Optimization
(1)
Data storage
Versioned API
Versioned API
Versioned API
Versioned API
Versioned API
Versioned API
Microservice Framework

## Slide 51
2.3 architecture and design
Model is composed of hierarchical composition of model entities
Each model entity has a generic set of properties
Special implementation of model entity types via inheritance
Strict separation of model component through API
Current implementation in C++
Geometric model functions (such as STEP import) based on OpenCascade
Model Management

## Slide 52: 2.3 architecture and design
User Interface
(1)
Versioned API
Model management
(1)
Generic visualization
(1...n)
Meshing
(1…n)
Result visualization
(1…n)
Simulator plugin
(1…n)
Automation and Optimization
(1)
Data storage
Versioned API
Versioned API
Versioned API
Versioned API
Versioned API
Versioned API
Microservice Framework

## Slide 53
2.3 architecture and design
Generic visualization based on Open Scene Graph (C++ implementation)
Scene is composed of visualization entities
Separated through API, but integrated with UI module in same process
Provides view management (selection, visibility)
Generic Visualization

## Slide 54: 2.3 architecture and design
User Interface
(1)
Versioned API
Model management
(1)
Generic visualization
(1...n)
Meshing
(1…n)
Result visualization
(1…n)
Simulator plugin
(1…n)
Automation and Optimization
(1)
Data storage
Versioned API
Versioned API
Versioned API
Versioned API
Versioned API
Versioned API
Microservice Framework

## Slide 55
2.3 architecture and design
Meshing module currently integrated with model component, will later on be separated in specific microservice
Mesh model generation based on OpenCascade boolean operations
Meshing currently based on gmsh
Implementation of meshing data structures does not rely on gmsh (exchange of meshing kernel possible)
Implementation done in C++
Currently limited to triangle / tetrahedral meshing only
Drives generic visualization module through API
Re-compiled version of gmsh for integration with model component‘s version of OpenCascade
Meshing

## Slide 56
2.3 architecture and design
Open Source software
Open Twin specific parts: MIT type license
Various Open Source type licenses for third party components
Managed on GitHub: https://github.com/pth68/SimulationPlatform
Content of development branch
(including 3rd party modules)

## Slide 57
Open twin introduction Agenda
Challenges
  1.1 Multi Domain and Multi Scale
  1.2 Computational Resources
  1.3 Data Management / Data Analytics
Open Twin
  2.1 System Requirements Overview
  2.2 Why Open Twin?
  2.3 Architecture and Design
Open Twin Status and Research
Next Steps








## Slide 58: 3. open Twin status

## Slide 59: 3. open twin status
User Interface
(1)
Versioned API
Model management
(1)
Generic visualization
(1...n)
Meshing
(1…n)
Result visualization
(1…n)
Simulator plugin
(1…n)
Automation and Optimization
(1)
Data storage
Versioned API
Versioned API
Versioned API
Versioned API
Versioned API
Versioned API
Microservice Framework








## Slide 60
2. open Twin research
Example: “SecuSiM” (cloud security)
Today:
  Cloud solutions provide efficient and scalable computational resources
  External (or public) clouds are hosted by service provider
  Application data needs to be uploaded to the cloud for running the simulations
  Data transfer from and to cloud is usually encrypted and safe enough
  How about the cloud system itself? Trusted service provider?
  So far, application data needs to be decrypted on cloud system for simulation
SecuSIM:
  Apply homomorphic encryption to run computations on the encrypted data
  The data is encrypted and decrypted only on client
  Matrix operations are performed on the encrypted data directly. Results can only be decrypted by the client
  The project will study the feasibility / performance of this technology for simulation algorithms (FIT-TD / FDTD)
  Robert Bosch GmbH supports this project through a letter of support

## Slide 61
Open twin introduction Agenda
Challenges
  1.1 Multi Domain and Multi Scale
  1.2 Computational Resources
  1.3 Data Management / Data Analytics
Open Twin
  2.1 System Requirements Overview
  2.2 Why Open Twin?
  2.3 Architecture and Design
Open Twin Status and Research
Next Steps









## Slide 62
4. Next steps
Project management
Various UI and usability improvements
Material management
Improved meshing control / parallelization
Integration of vtk for post processing visualization & pixel streaming
1D Graph library for post processing visualization
Generic simulator plugin (e.g. Studio Suite integration)
Automation (Python based) and optimization modules
Physics coupling module (based on preCICE)
Build automation / Doxygen / Unit-testing / Deployment
… tbd …

## Slide 63: Thank you!
Frankfurt University of Applied Sciences, Faculty 2, ©2020 Prof. Dr.-Ing. Peter Thoma
63